## Slide 1: KAĞAN ÖZASLAN CFO

## Slide 2
Video Transmission
Command Transmission

## Slide 3: Video Transmission
5.8 Ghz
600mw Transmitter (TS5828)
40 Channel
27.5 dBm
170 degree camera

## Slide 4: Video Transmission
5.8 Ghz Receiver (ROTG02)
Easy to use
Plug and Play with usb cable
150 Channel

## Slide 5: Test Results
Outdoor = 500 m
Indoor = 50 m (from E Building Top Floor to D Building Study Hall)

## Slide 6: Test Results
Outdoor = 500 m
Indoor = 50 m (from E Building Top Floor to D Building Study Hall)
Improvement Option
  5.8G Amplifier
  27dBm to 34 dBm

## Slide 7: Command Transmission
2.4Ghz band
NRF24L01+ module
  Very cheap (less than $2)
  Compatible with high gain antennas
  2.4ghz antennas are also very cheap
  Secure communication protocol
  100mW, legal to use

## Slide 8: Command Transmission

## Slide 9: Test Results
NRF modules with 15dBi Linear Antennas
Outdoor = 1 km
Indoor = 100 m

## Slide 10: Communication Protocol

## Slide 11
Preamble: Shows beginning of a packet.
Address: Shows the network pipe address.
Packet Control: Settings section.
Payload: Sending data is stored inside. Upon 32 byte.
CRC: Cyclic redundancy check for error detection.

## Slide 12: User Side